## Slide 1: Design Assistance System 2 (DASY2)
Sergii Bogomolov
Czech Technical University in Prague
Prague, 12 March 2013

## Slide 2: Outline
Introduction
DASY overview
Problem: new requirements
Solution: DASY2
  New approach to model structure
  New numerical solver
  New optimization algorithm
Conclusion & Future work

## Slide 3: Introduction
It is advantageous to have some tools that can assist in design process
Minimize time, required for an engineer to make specific improvements in the model and then analyse it
Another demand to such system is a high level of flexibility
One of the most difficult moments in concept design is the starting point
Notes: Design process requires a great amount of human time and computational power. That is why it is advantageous to have some tools that can assist in design process. One of the tasks for such tool would be to minimize the time, required for an engineer to make specific improvements in the model and then analyse it. It can be done with help of design network approach. This means that engineer can focus on some narrow area or set of parameters and work with them letting the system to take care of all other.
Another demand to such system is a high level of flexibility. Even if an engineer needs to cover only one field of possible applications of this system (for example internal combustion engines), one still needs the high level of flexibility, because standard components and structure of the engine are changing and in five or ten years fixed design templates will not be able to describe new models and structures.
In addition, one of the most difficult moments in concept design is the starting point. If there would be some examples of previously created components, parts or assemblies, carefully stored in knowledge database, then designer could take one of them and use it as a starting point for his or her own concept.
System that aims to assist in design process should be able to store these examples with all geometrical parameters and their description in knowledge database.

## Slide 4: DASY overview
What is DASY?
Knowledge
Database
DASY
Notes: What is knowledge database? Well, it is a storage for all knowledge, innovations and progress. All designs, successful or not, are stored in one place with all support information like CAD models, drawings or specifications, results of FEM and CFD calculations, may be some mathematical or physical models. Everything that is somehow related to current design task is stored right there, right where you expect it to be. If in ten years engineer or one of his/her followers will have a similar task, he/she will not have to start from scratch, everything that has already been done in this direction is stored and ready to be used.

## Slide 5: DASY overview
The model in DASY is represented as a set of components. Each component has a set of parameters, structural requirements and files related to it. Each component can have subcomponents and subassemblies. All components are stored in the library and can be divided into classes.
Notes: The model in DASY is represented as a tree of components. Each component has a set of parameters, structural requirements and files related to it. Each component can have subcomponents and subassemblies. If component has a subcomponent it becomes an assembly. All components are stored in the library and can be divided into classes. Each class also can have some parameters and requirements that will be common for all components of this class. The structure of components in the model is totally flexible. However, it is possible to specify some structural requirements for components and classes of components. For example, it is possible to say that engine component class will require engine block component class. In this structural requirement any component of Engine class will require one component from Engine Block class as its subcomponent. Also some additional parameters can be specified in these requirements. Structural requirements are a very powerful approach that allows one that is creating components to specify the structure of future assembly or subassembly be specifying required components. From the other side this is very flexible structure, because one can specify only component class that is required (engine block) and any component from this class will fit. Another degree of flexibility is that all requirements can be changed, removed or added and even if not, not all of them have to be satisfied.

## Slide 6: DASY overview
To any level of component or model, the computational, design or experimental methods are linked. The methods may be elaborated at different levels of physical profoundness. The deeper to the substance of phenomena description the method is extended to, the more data are usually called for as input parameters.
Input and output parameters for one method should be distinguished, but output of one method can be an input for another.
Notes: To any level of component or model, the computational, design or experimental methods are linked. The methods may be elaborated at different levels of physical profoundness. The deeper to the substance of phenomena description the method is extended to, the more data are usually called for as input parameters. E.g., the cranktrain may be described either by simple algebraic system of static and dynamic force balance (AE) or by differential algebraic equations with ordinary differential equations (DAE or ODE) involving the masses and stiffnesses (typically in some multi-body dynamics approach) or even by the partial differential equations (PDE) solved by, e.g., finite element methods (FME) for the coupled dynamics of a cranktrain and cylinder block/crankcase movement.
Components are interconnected with parameters. The parameters network is common for each model so all parameters and dependencies between them basically form connections between components. Each parameter can be used as an input or output for some method.

## Slide 7: DASY overview
When the model is composed from the components, all parameters from all components form a design network. This network can consist of parameters, dependencies, constraints and requirements.
2011-37-0030
Notes: When the model is composed from the components, all parameters from all components will form a design network. This network can consist of parameters, dependencies, constraints and requirements.
Parameters are design variables. They can have different values, such as numbers from some range, or from predefined list. They also can be computed according to dependencies. Parameter values range is defined by constraints.
Constraints are limitations for parameters values that can’t be violated. Requirements are the opposite – values of parameters that should be assigned. It is necessary to distinguish between requirements on this figure (required values for some parameters) and structural requirements in components (when component requires some other components as a subcomponent).
Dependencies are methods that take some parameters as input and some as output.

## Slide 8: What next?

## Slide 9: New requirements
We want to have scalable models to be even more flexible when designing. This can be achieved using separate parameter namespaces for each component.
We want to solve reverse task without model redefinition. This can be done using numerical solvers and descriptive model definition instead of input-output based.

## Slide 10: New approach to model structure
3. Log window
1. Blocks Library
2. Model window
Every block and connection in the model are represented with one or several relations.

## Slide 11: New approach to model structure
There are no input and output parameters, but left and right instead.
Flexible and clear control of where and what parameters to show.
Parameters are discovered automatically by parsing and simplifying algebraic relations.
1. Block parameters
2. Algebraic relations

## Slide 12: New approach to model structure
One place to manage parameter values and limits.
Definition of known and unknown parameters with respect to relations. DASY2 automatically finds dependent parameters.

## Slide 13: New numerical solver
To deal with time-consuming external computations (e.g. CFD, FEM), external methods are represented as pre-computed local response surfaces.
Builds a system of nonlinear algebraic equations from all blocks and connections and solves it using numerical iterations (different algorithms can be supported).
This allows having a descriptive model definition instead of input-output based.
This also allows solving both direct and reverse tasks without model redefinition.

## Slide 14: New numerical solver
Gradient descent is a first-order optimization algorithm.
It is based on the observation that if the multivariable function F(x) is defined and differentiable in a neighborhood of a point a, then F(x) decreases fastest if one goes from a in the direction of the negative gradient of F at a.
With this observation in mind, one starts with a guess for a local minimum of F and considers the sequence , , , … such that

## Slide 15: New numerical solver
a
b
a = c1 + c2*cos(phi)
a
c1
phi
c2
some computation
that gives b(c3, c4)
Connection:
Algebraic relation:
External method:
b
c4
c3

## Slide 16: New optimization algorithm
Improved Strength Pareto Evolutionary Algorithm 2 (SPEA2+):
Uses a regular population and two archives to hold diverse solutions in the objective space and variable space.
During fitness assignment for each individual both dominating and dominated solutions are taken into account.
Environmental selection is used during archives update. This allows to keep outer solutions in the archive in order to obtain a good spread of non-dominated solutions.
Neighborhood crossover, which crosses over individuals close to each other in objective space. In neighbourhood crossover, individuals that match in the search direction are crossed over to generate offspring that are similar to the parent.
Mating selection, which reflects all archived good individuals in the search. all of the archive is copied to the population used in the search.

## Slide 17: New optimization algorithm
Step 1: Initial population is generated, .
Step 2: Fitness values of all individuals in , and are calculated with fitness assignment method.
Step3: All non-dominated individuals in , and are copied to and . If the number of individuals of and has exceeded , archive truncation in objective space is applied to the individuals in , and archive truncation in variable space is applied to the individuals in to reduce the number of individuals. If the number of individuals of or is less than , individuals with good fitness from , and are used to fill and .
Step 4: Terminate the search if or other termination conditions are met.
Step 5: is generated by copying . The neighborhood crossover and mutation operations are performed. Return to step 2 with

## Slide 18: Fitness assignment method
Each individual in both archives and population is assigned a strength value , representing the number of solution it dominates:
where denotes the cardinality of a set, stands for multiset union and the symbol corresponds to the Pareto dominance relation.
On the basis of the values, the raw fitness of an individual is calculated:
That is the raw fitness is determined by the strengths of its dominators in both archive and population.

## Slide 19: Fitness assignment method
Although the raw fitness assignment provides a sort of niching mechanism based on the concept of Pareto dominance, it may fail when most individuals do not dominate each other. Therefore, additional density information is incorporated to discriminate between individuals having identical raw fitness values. Density is estimated as the inverse of the distance to k-th nearest neighbor. The density is defined by
In the denominator , two is added to ensure to ensure that its value is greater than zero and that .

## Slide 20: Environmental selection
During environmental selection, the first step is to copy all non-dominated individuals, i.e., those which have a fitness lower than one, from archive and population to the archive of the next generation:
If the non-dominated front fits exactly into the archive the environmental selection step is completed.
If the archive is too small – the best dominated individuals in the previous archives and population are copied to the new archives.
If the archive is too large an archive truncation procedure is invoked which iteratively removes individuals from and until their sizes will match .

## Slide 21: Archive truncation
For archive , at each iteration that individual is chosen for removal for which for all with
Where denotes the distance of to its k-th nearest neighbor in . In other words, the individual which has the minimum distance to another individual is chosen at each stage; if there are several individuals with minimum distance the tie is broken by considering the second smallest distances and so forth.

## Slide 22: Neighborhood crossover
In multi-objective GAs, effective crossover often cannot be performed, as the searching directions of each parent individual are very different from one another. Neighborhood crossover performs crossover with individuals neighboring each other in objective space. In neighborhood crossover, individuals that match in the search direction are crossed over to generate offspring that are similar to the parent.
Neighborhood crossover is performed as follows:
Step 1: Sort the population with one of the function values. The function value used in the sort is altered each generation.
Step 2: Neighborhood shuffle is performed for the sorted population.
Step 3: Select -th and -th items as parents and crossover is performed.
In neighborhood crossover, individuals that are next to each other within the population sorted based on arbitrary function values are defined as neighboring individuals. To avoid crossing over with the same individuals, the neighborhood shuffling operation is applied after sorting. Neighborhood shuffling counterchanges individuals in the randomized range, which is less than 10% of the population size.

## Slide 23: Conclusion
New requirements showed some problems with original approach.
New approach is developed and implemented in the next generation system – DASY2. Now model has a descriptive definition.
New numerical solver with the new descriptive model definition allows solution of both direct and reverse tasks without model redefinition.
New advanced optimization algorithm is implemented.

## Slide 24: Future work
Reimplementation of features from the first DASY.
Implementation of local response surfaces approach for time consuming external computations.
Implementation of different numerical solver algorithms.
Implementation and comparison of different optimization algorithms.

## Slide 25: Acknowledgment
This work has been realized using the support of EU Regional Development Fund in OP R&D for Innovations (OP VaVpI) and Ministry of Education, Czech Republic, project # CZ.1.05/2.1.00/03.0125 Acquisition of Technology for Vehicle Center of Sustainable Mobility.
This support is gratefully acknowledged.

## Slide 26
Thank you for your attention!
E-mail: sergii.bogomolov@fs.cvut.cz
Design Assistance System 2 (DASY2)