## Slide 1: EARLY STAGE OPTIMIZATION OF CRANKSHAFT MASS USING DESIGN ASSISTANCE SYSTEM (DASY)
Sergii Bogomolov, Jan Macek, Antonin Mikulec, Tomas Novotny, Josef Kazda
Czech Technical University in Prague
Maastricht, 4 June 2014

## Slide 2: Outline
Introduction
FE Model
  Full Model
  Simplified Model
Design Assistance System (DASY)
  Description
  Optimization
Conclusion

## Slide 3: Introduction
Crankshaft is one of the most critical and important parts of the internal combustion engine (ICE) and its proper design is an important task.
During this study we wanted to optimize crankshaft design in a way that the optimized design can still be used in the original engine. This has limited the selection of possible changes to the design.

## Slide 4: FE Model
Real crankshaft was measured and modelled in Abaqus.
Model is detailed and good for one-time computations.
Can be used to verify optimized design.
Notes: A real crankshaft was measured and modelled in ABAQUS software. This model is quite detailed, has many elements and is good for one-time computations. But for optimization purposes a simplified model which can be computed reasonably fast is needed.

## Slide 5: FE Model (simplified)
Approaches used to reduce computational time:
increase the size of elements
model only part of the crank
use linear elements instead of quadratic
Notes: In order to reduce computational time the number of elements must be reduced. One approach is to increase the size of elements. This will decrease accuracy of the results, but we can always verify final design using more accurate model. Second approach is to use only part of the model with corresponding boundary conditions to define planes of symmetry. In this study, combination of both approaches was used.
Model of crank has two planes of symmetry. Boundary condition to represent the plane of symmetry restricts displacement in the direction of normal to the plane of symmetry and all rotations except the rotation around the normal to the plane of symmetry.
Another simplification that can be done is to use linear elements instead of quadratic ones. All listed simplifications have led to a model that can be computed in 21 seconds compared to 12 minutes for the original model on the same machine.
To automate the process of parameters updating and model computation, a script in Python programming language was written. Python is natively supported by ABAQUS, which allows direct interaction with the model.

## Slide 6: Design Assistance System (DASY)
Knowledge
Database
DASY
Notes: What is knowledge database? Well, it is a storage for all knowledge, innovations and progress. All designs, successful or not, are stored in one place with all support information like CAD models, drawings or specifications, results of FEM and CFD calculations, may be some mathematical or physical models. Everything that is somehow related to current design task is stored right there, right where you expect it to be. If in ten years engineer or one of his/her followers will have a similar task, he/she will not have to start from scratch, everything that has already been done in this direction is stored and ready to be used. DASY is an implementation of these concepts.

## Slide 7: Design Assistance System (DASY)
The key features of DASY are:
Creating components and assemblies
Storing, grouping and reusing created components
Storing, grouping and reusing created models
Direct interaction with CAD systems via plugins
Interaction with external software via Input/Output files and external methods plugins
Multi-objective optimization
Notes: The key features of DASY are:
Creating components and assemblies.
Storing, grouping and reusing created components.
Storing, grouping and reusing created models.
Direct interaction with CAD systems via plugins.
Interaction with external software via Input/Output files and plugins.
Multi-objective optimization.
DASY has a graphical user interface developed using Windows Forms. All interactions with models, components, parameters and other data are performed using specialized dialog windows or through main and popup menus.

## Slide 8: Design Assistance System (DASY)
The model in DASY is represented as a set of components. Each component has a set of parameters. Each component can have subcomponents and subassemblies. All components are stored in the library and can be divided into classes.
Notes: The model in DASY is represented as a tree of components. Each component has a set of parameters, structural requirements and files related to it. Each component can have subcomponents and subassemblies. If component has a subcomponent it becomes an assembly. All components are stored in the library and can be divided into classes. Each class also can have some parameters and requirements that will be common for all components of this class. The structure of components in the model is totally flexible. However, it is possible to specify some structural requirements for components and classes of components. For example, it is possible to say that engine component class will require engine block component class. In this structural requirement any component of Engine class will require one component from Engine Block class as its subcomponent. Also some additional parameters can be specified in these requirements. Structural requirements are a very powerful approach that allows one that is creating components to specify the structure of future assembly or subassembly by specifying required components. From the other side, this is very flexible structure, because one can specify only component class that is required (engine block) and any component from this class will fit. Another degree of flexibility is that all requirements can be changed, removed or added and even if not, not all of them have to be satisfied.

## Slide 9: Design Assistance System (DASY)
To any level of component or model, the computational, design or experimental methods are linked. The methods may be elaborated at different levels of physical profoundness. The deeper to the substance of phenomena description the method is extended to, the more data are usually called for as input parameters.
Input and output parameters for one method should be distinguished, but output of one method can be an input for another.
Notes: To any level of component or model, the computational, design or experimental methods are linked. The methods may be elaborated at different levels of physical profoundness. The deeper to the substance of phenomena description the method is extended to, the more data are usually called for as input parameters. E.g., the cranktrain may be described either by simple algebraic system of static and dynamic force balance (AE) or by differential algebraic equations with ordinary differential equations (DAE or ODE) involving the masses and stiffnesses (typically in some multi-body dynamics approach) or even by the partial differential equations (PDE) solved by, e.g., finite element methods (FME) for the coupled dynamics of a cranktrain and cylinder block/crankcase movement.
Components are interconnected with parameters. The parameters network is common for each model so all parameters and dependencies between them basically form connections between components. Each parameter can be used as an input or output for some method.
The tool is responsible for two major tasks. The first one is to provide a flexible knowledge database management tool. The second one is to provide an engineer with a framework to interact with a number of external software along with implemented algorithms and automate these interactions to provide an option for design optimization.
The first task requires storage and management of design data. Current task is complicated by required high level of flexibility. This means that fixed database structures cannot be used. It was decided to store data in Extensible Markup Language (XML) format. XML is a set of rules for encoding documents in machine-readable form. It is defined in the XML 1.0 Specification produced by the World Wide Web Consortium (W3C), and several other related specifications. The design goals of XML emphasize simplicity, generality, and usability. It is a textual data format which allows editing by hand. Although the design of XML focuses on documents, it is widely used for the representation of arbitrary data structures.
It is also important to save the path to the final design, so it will be possible for successors to understand what decisions were made and why. This can be done by saving intermediate versions of designs and using commentaries. In the tool, any parameter, component, method or model can have a description that may explain why some approach is used or why some modification was made.
Second task requires a general transparent interface for end-user to use external software from DASY framework. This is done through methods approach. Method is a transfer function from input to output parameters. At the current stage of development, the following methods are implemented in the tool:
Equation method defines a relation between parameters using simple algebraic equations.
Input & Output Files method interacts with external software using input and output files approach.
CAD Model is also a method which allows updating of CAD model. This method utilizes an implemented plugins system, which means that there is no difference what CAD system is used as long as required plugin is present. All interactions with CAD systems are generalized with a common interface so an engineer can use any units. No conversions are applied.
External methods allow using user-defined algorithms and also can be a layer between the tool and external software.

## Slide 10: Methods Overview – Plugins System
CATIA Part
External Method 1 Plugin
Pro/E CAD Plugin
CATIA Part
CATIA Part
Pro/E Model
Pro/E Model
Pro/E Model
Other CAD Plugin
DASY
External Method 3 Plugin
External Method 2 Plugin
External Software 1
CATIA CAD Plugin
External Software 3
External Software 2
Other Model
Other Model
Notes: Now I would like to tell about plugins systems. In fact DASY has 2 separate plugins systems, but it is very transparent for end user. What is a plugin? Plugin is a standalone .dll library with some code in it. There are some interfaces that must be adopted by this library (one interface per plugin type), so DASY would know how to communicate with it. So interface is like a common language that can be used for communication. But inside plugin can have any algorithms that are needed. There are absolutely no limitations.
Let’s imagine that we have our model in DASY and it works fine. Now we want to assign several CAD models to update them with parameters from DASY. Let say, we’ve found some parameter values for an optimal shape and want to see how it will really look like. So how can we do this? 1st type of plugins in DASY is CAD plugins. CAD plugins are responsible for interaction with specific CAD software providing DASY with common interface to work with them. So having plugins for corresponding CAD models types will allow us to use this models in DASY. This approach is very flexible and allows to take into account some aspects of specific CAD systems. For example, Pro/E files have double extension, like .prt.11 or asm.6. Another specific aspect of Pro/E CAD system is that sometimes to update all parameters and geometry inside model it needs to regenerate its features twice. After first regeneration the model is not fully updated. This is caused by its internal parameter update algorithms. These aspects were successfully taken into account in developed Pro/E plugin and DASY or engineer that works with it does not have to know about these specialities. More about this type of plugins later.
Now, let’s imagine that you have some knowhow. You do not want to share the algorithm, but you want your partners to use it so all can benefit. What can you do? Here the 2nd type of DASY plugins comes in to play. So called external methods are plugins that adopt a common interface, but inside it’s a black box. External method is a .dll library, like a CAD plugin. It can have a lists of input and output parameters and your know-how buried inside. It means that someone who’ll get this plugin from you will be able to use it with DASY by providing his input and getting the output. But your know-how will not be exposed, it will still be in that black box, called external method plugin.
That’s a very flexible system that can cover any task and DASY can automatically pick up and use any number of CAD or external method plugins without any modifications. As I’ve just said, the only demand for the plugin is to adopt a common for this plugin type interface, so DASY will know how to communicate with it. But there are no limitations for what will be coded after this. For example, external method plugin can use some external software package or even a couple of them.

## Slide 11: Optimization
1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1
Notes: The genetic algorithm is all about evolving through generations. Generation is a set of genomes. Each genome is a set of chromosomes (parameter values in our case), or in different words each genome is a solution. The task is to find the best solution. This is done using fitness function. Fitness function should be able to evaluate a fitness of genome. The higher fitness is better. This approach allows us to compare genomes and say which one is better.
At the beginning we have a 1st generation composed from randomly generated genomes. Each genome is a solution inside our solution space. This means that all this solutions are feasible. This must be preserved to get a feasible results at the end of optimization.
We select two genomes that will be parents. The selection procedure may be different: roulette selection, tournament selection or selection based on Pareto set for multi-objective optimization, but the idea is that the most of the selected genomes must be the fittest ones. Not all of them, because we do not want to stuck in some local minimum area.
Now we want to crossover these two parents. To do this, we randomly select a cutting point and then combine them into two new child genomes. Sometimes there is no crossover between two parents. In this case two child genomes are equal to their parents. The probability of crossover is determined by crossover rate.
Then mutation can happen. Mutation is a random modification of some chromosome in genome. The probability of mutation is determined by mutation rate.
These steps are repeated until the population of children reaches the population size. When this happens, children generation becomes a current one and this process starts from the beginning.
The idea is that each next generation is fitter than the previous, because mostly the best genomes from past generation were selected as a parents for this generation.

## Slide 12: Optimization
Optimization objectives
Genetic Algorithm parameters
Optimization progress information
Pareto set
Notes: Optimization in DASY is multi-objective. In this figure optimization start dialog window is shown. We define the optimization objectives here and specify the Genetic Algorithm parameters. This parameters are crossover and mutation rates, population size, number of generations and global Pareto set size. When we press start, the optimization process begins. In the second figure we can see an optimization process information: number of generations completed, current generation Pareto set size, global Pareto set size, average time required for one generation, time elapsed and approximated time till the end of optimization.
When optimization is complete we can review the optimization process statistics and proceed to the next window which draws Pareto sets. In this window we can graphically select an interesting solution and set all parameter values according to it.

## Slide 13: Optimization
Template of input file for ABAQUS, which is a Python script in this case
Rules defining the position of output parameter values in output file
Commands to execute in order to start computation
Notes: In order to perform optimization of crankshaft using DASY, the model of crankshaft should be connected to DASY model using Input & Output Files method. This method requires:
Template of input file for ABAQUS, which is a Python script in this case (Fig. 9). Text marked with green will be substituted with input parameter values automatically.
Rules defining the position of output parameter values in output file (after ABAQUS computation, Fig. 10).
Commands to execute in order to start computation.

## Slide 14: Optimization
Parameters used for optimization:
width of cheek
length of main journal
diameter of main journal
fillet radius
As a result of this optimization, 281.6 grams of material were saved for one crank.
Notes: Parameters used for optimization are shown in figure. Following parameters were selected as variables:
width of cheek, LCSCHE1;
length of main journal (constraint in a way that LCSJOL + LCSCHE1 is constant), LCSJOL;
diameter of main journal, DCSJO;
fillet radius, RR.
The result of the optimization is a Pareto front shown in figure. Based on material strength and safety margins, only one solution from this set was selected.

## Slide 15: Conclusion
Finite-element (FE) model of crankshaft was created in ABAQUS using geometry, measured on a real crankshaft.
Simplified FE model of one crank was created using two planes of symmetry in order to reduce computational time.
Preliminary optimization using DASY software was performed with two optimization goals: minimize mass and stress.
As a result of this preliminary study, 1080 grams of material were saved, which is more than 6% of the original crankshaft mass.

## Slide 16: Acknowledgments
Technological Agency, Czech Republic, programme Centre of Competence, project #TE01020020 Josef Božek Competence Centre for Automotive Industry.
EU Regional Development Fund in OP R&D for Innovations (OP VaVpI) and Ministry of Education, Czech Republic, project #CZ.1.05/2.1.00/03.0125 Acquisition of Technology for Vehicle Center of Sustainable Mobility.

## Slide 17: EARLY STAGE OPTIMIZATION OF CRANKSHAFT MASS USING DESIGN ASSISTANCE SYSTEM (DASY)
Thank you for your attention!
E-mail: sergii.bogomolov@fs.cvut.cz